## Slide 1: Propositions for FDSN and Marine Seismology Standards
The FDSN WG5 Action Group on Marine Seismology Metadata and Data Standards*
*Wayne C. Crawford1, Kasey Aderhold2, Yinshuang Ai3, Jerry Carter2, John A Collins4, Carlos Jorge Corela5, Susanne Hemmleb6, Takehi Isse7, Joel D. Simon8, Maria Tsekhmistrenko9
1IPGP, CNRS & Univ. Paris Cité; 2Earthscope Consortium; 3Inst Geol. & Geophys., Chinese Acad. Of Sci.; 4Woods Hole Oceanographic Inst.; 5Inst. Dom Luiz, Fac. Ciencias da Univ. Lisboa; 6Helmholtz Centre Postdam GFZ German Research Center for Geosci.; 7Univ. Tokyo; 8Princeton Univ.; 9Univ. College London

## Slide 2: Overview
Goal: Define/identify standards for marine seismology data and metadata
Time Period: Sept 2023-present (2 years, bimonthly meetings)
Members: 4 North America, 4 Europe, 2 Asia
Subjects:
  StationXML standards
  miniSEED standards
  Source identifier standards
  Software

## Slide 3: Major Issues
Clock drift
Leapseconds
Data completeness
Leveling systems
Positions and Orientations

## Slide 4: Outputs
Proposals for new FDSN standards (or documentation)
  Source identifiers
  StationXML
  miniSEED?
Document reference/guide for marine seismology data providers
Identification of fields that still need work

## Slide 5: Proposals: Source Identifiers
In documentation
  If a component’s angle relative to another component is known, but it’s absolute angle is not, the given angle should be the relative angle, and “plusError” and ”minusError” should be set to 180.
  if there are two orthogonal horizontal channels that are not known to be aligned to N and E, they be named 1 and 2, with 2 oriented 90° clockwise of 1 when viewed from above.
  If the vertical channel is inverted, name it “3”

## Slide 6: StationXML metadata
Interim StationXML elements:
  Used while waiting/proposing a new StationXML element. Elements are :
  A JSON string in a <Comment><Value> or <Equipment><Description>

## Slide 7: Proposal: StationXML metadata
Clock drift
  New Element at Station level
      <ClockDrift>
      <Type>str</Type> # “piecewise_linear”, “cubic_spline” or “polynomial {a0} {a1} {a2}…”
      <Instrument>
      <Model>str</Model>> # e.g. “Seascan MTCv4.1”
      <NominalDriftRate>float</NominalDriftRate> # e.g. 10^-8
      <Reference>str</Reference> # e.g. “GNSS”, or “cross-correlated station XXX”
      <SyncTime>
      <Instrument>datetime</Instrument><Reference>datetime</Reference>
      <\SyncTime>
      <SyncTime> <Instrument>datetime</Instrument><Reference>datetime </Reference><\SyncTime>
      ...
      </ClockDrift>
  Interim Element:
<Comment subject=“Clock drift”><Value>{type: {“piecewise_linear”}, instrument: {model: 'Seascan MCXO’, nomimal_drift_rate: 1e-8}, reference: ‘GNSS’, synctimes: [ {instrument:"2016-09-10T00:00:00Z", reference: "2016-09-10T00:00:00Z”},_instrument:"2017-01-12T00:00:01Z", reference:"2017-01-12T00:00:00.415Z »}, {instrument:"2017-07-13T11:25:01Z", reference:"2017-07-13T11:25:00.6189Z »}]}</Value></Comment>

## Slide 8: Proposal: StationXML metadata
Clock drift
  If we expect drift but no drift was measured
    Empty element (or allow <Instrument> subelement?)
<ClockDrift></ClockDrift>
  Documentation: The instrument sync times must be leapsecond-corrected
GFZ-style Instrumentation IDs

## Slide 9: Proposal: StationXML metadata
Leveling system
  Proposed new element at Channel-level
    LevelerType element derived from EqupimentType, with an additional <Relevel> subelement:
  <Leveler>
  <Relevel>
      <Threshold units=‘degrees’>float</Threshold> # degrees from level at which relevel is triggered
      <Accuracy units=‘degrees’>float</Accuracy> # relevel returns to at most this offset from level
      <MaxInterval units=“hours”>float</MaxInterval> # longest time passed between level checks
      </Relevel>
      </Leveler>
  Interim Element
  <Equipment>
<Type>Leveler</Type>
<Description>{relevel: {threshold.deg: 2.5, accuracy.deg: 0.25, max_relevel_interval.h: 168}, description: ‘SIO-Nanometrics BBOBS leveling system’}</Description>
<Manufacturer>Scripps Inst. Oceanography</Manufacturer>
<SerialNumber>FR02</SerialNumber>
</Equipment>

## Slide 10: Proposal: StationXML metadata
Documentation
  Add a pressure sensor to the StationXML Response Examples
    Hydrophone
    Also Differential and Absolute Pressure Gauges?

## Slide 11: Proposal?: miniSEED metadata
Is there a way to specify when data is good or bad?
  Existing fields?
    miniSEED2 : Field 14 byte 1 = 1 (“Amplifier saturation detected”)?
    miniSEED3: {‘FDSN’: {“Flags”: {“MassPositionOffscale”: true}}}
  New miniSEED3 field?
    {‘DataBad’: true}?

## Slide 12: Marine Documentation: miniSEED data
Use msmod for leap second correction
  Can it handle incorrect leap second position?
Using FDSN/Recenter/Sequence/{BeginTime, EndTime} for relevels (Type=“Gimbal”) and mass centers (Type=“Mass”)
  Including shell/Python example

## Slide 13: Marine Documentation: source identifers
All proposed documentation changes

## Slide 14: Marine Documentation: StationXML
Positions and Orientation
  Recommend setting the plusError, minusError and measurementMethod sub-elements to specify uncertainties in Latitude, Longitude, Elevation, Dip and Azimuth, and how these values were estimated.
Deployments in lakes
  Remind that the <WaterLevel> element should be set to the elevation of the lake surface
Data completeness
  We recommend keeping all of the recorded data, including "noisy" or "bad".
    Only if we can indicate bounds of good data?
      miniSEED3
        {“FDSN”:{Flags:{"MassPositionOffscale": true}}}?
        {“QualityControl”:{“BadData”:true}}?
Response Examples
  Of any pressure sensor (hydrophone, differential pressure gauge, absolute pressure gauge) not added to StationXML Response Examples documentation

## Slide 15: Marine Documentation: distinguishing clock correction levels in miniSEED DATA
The correction is the seconds to add to the original time
 | miniSEED2 | miniSEED3
NOT CLOCK CORRECTED | Quality flag = ‘D’ Field 12 bit 1 = 0 | Root/FDSN/DataQuality = ‘D’ -or- DataPublicationVersion=1
CLOCK CORRECTED | Quality flag = ‘Q’ Field 16 = correction in 0.00001s Field 12, bit 1 = 1 | Root/FDSN/DataQuality = ‘Q’ -or- DataPublicationVersion=2+ Root/Time/Correction – correction in s
Unmeasured drift | Quality flag = ‘D’ Field 14, bit 7 = 1 Blockette 500, field 10 = “unmeasured clock drift, expected order = 10^-XX” | Root/FDSN/DataQuality = ‘D’ ?????

## Slide 16: Marine Documentation: distinguishing clock correction levels in miniSEED DATA
RESAMPLED data
  Needs another channel code to specify modified data (none currently in Source Identifiers)
  Or use extra header, as suggested in miniSEED3 “Data publication version” description:
    {“ResampledData”: true}?

## Slide 17: Marine Documention: Other information
Remind that if CLOCK CORRECTED and NOT CLOCK CORRECTED are provided in SDS format, they must be in the same file
Recommend providing CLOCK CORRECTED
Order in which to perform leap second and clock drift corrections
How to request additions to StationXML
New msmod versions: drift correction and leapsecond addition/correction
Saving processing steps information (Provenance/Reproducibility)
Station names for repeated deployments
Geophone wiring and polarity
Set miniSEED3 sampling rate to exact value (msmod capability)

## Slide 18: Open issues
Dataloggers that correct leap seconds
Dataloggers that output StationXML metadata
  List and conformity
Optional methods for applying clock drift + leapsecond corrections

## Slide 19: Software
There are many processes that need to be applied to most marine data (see “Subjects” at right)
Currently have a document with a list of known software (including msmod)

## Slide 20: Going forward
Submit proposals to FDSN WG2
Write and publish marine documentation
Create software github + action group
  Create an FDSN github site with the above list and wiki to allow users to add other software
  Create an Action Group to create
    Rules for validate software
      Well documented (readthedocs?)
      Easy Installation (conda, pip, simple Make…)
      Verified on Linux + Windows + macOS + ???
    List of Validated software
    Integrated software? (would need funding for software engineer)